## Slide 1: OLED1 Integration
Martin Ruppert

## Slide 2: OLED1 Xplained Pro - SSD1306

## Slide 3: Configure the SERCOM0 with MCC

## Slide 4: Configure Pins

## Slide 5: LED‘s and Buttons

## Slide 6: GFX Mono Library

## Slide 10: Add gxf_mono Glue
\src\gfx_mono\gfx_definitions.h
#include "../peripheral/port/plib_port.h"
#include "../peripheral/sercom/spi_master/plib_sercom0_spi_master.h"
#include "../system/time/sys_time.h"
#define GFX_DELAY_FUNCTION(x) \
{ \
SYS_TIME_HANDLE tm_hdl; \
SYS_TIME_DelayMS ( x, &tm_hdl ); \
while(SYS_TIME_DelayIsComplete(tm_hdl) == false); \
}
#define GFX_SPI_WRITE_FUNCTION(x,y) SERCOM0_SPI_Write(x,y)
#define GFX_SPI_IS_BUSY() SERCOM0_SPI_IsBusy()
#define GFX_DISPLAY_RESET_CLEAR() DISPLAY_RESET_Clear()
#define GFX_DISPLAY_RESET_SET() DISPLAY_RESET_Set()
#define GFX_DISPLAY_SS_N_CLEAR() DISPLAY_SS_N_Clear()
#define GFX_DISPLAY_SS_N_SET() DISPLAY_SS_N_Set()
#define GFX_DATA_CMD_SEL_CLEAR() DATA_CMD_SEL_Clear()
#define GFX_DATA_CMD_SEL_SET() DATA_CMD_SEL_Set()

## Slide 11: gfx_mono Initialization
Add GFX Init at the end of SYS_Initialize
void SYS_Initialize ( void* data )
{
...
init system function
...
APP_Initialize();
NVIC_Initialize();
gfx_mono_ssd1306_init();
gfx_mono_print_scroll("LAN867x PLCA Node: %d",DRV_ETHPHY_PLCA_LOCAL_NODE_ID);
gfx_mono_print_scroll("%s",TCPIP_NETWORK_DEFAULT_MAC_ADDR_IDX0);
gfx_mono_print_scroll("%s",TCPIP_NETWORK_DEFAULT_IP_ADDRESS_IDX0);
}

## Slide 12: Wait 1000 milli seconds
SYS_TIME_HANDLE tm_hdl;
while(1){
SYS_TIME_DelayMS ( 1000, &tm_hdl );
while(SYS_TIME_DelayIsComplete(tm_hdl)==false);
LED3_Toggle();
}
SYS_TIME_DelayMS ( 1000, &tm_hdl );
while(1){
if(SYS_TIME_DelayIsComplete(tm_hdl)==true){
LED3_Toggle();
SYS_TIME_DelayMS ( 1000, &tm_hdl );
}
}

## Slide 13: Add Virtuel UART Receive Funtion
„send to terminal commands from firmware“
\peripheral\sercom\usart\plib_sercom1_usart.c
void SERCOM1_USART_Virtual_Receive(char *str) {
while (*str!=0) {
if (SERCOM1_USART_RxPushByte(*str) == true) {
SERCOM1_USART_ReadNotificationSend();
}
str++;
}
}
\peripheral\sercom\usart\plib_sercom1_usart.h
void SERCOM1_USART_Virtual_Receive(char *str);

## Slide 14: Add Button Poll and Action
{
static int old_but1 = 0;
int temp_but1 = BUTTON1_Get();
if (temp_but1 && !old_but1) {
LED1_Set();
}
if (!temp_but1 && old_but1) {
LED1_Clear();
SERCOM1_USART_Virtual_Receive("iperf -s\n");
gfx_mono_print_scroll("iperf TCP server");
}
old_but1 = temp_but1;
static int old_but2 = 0;
int temp_but2 = BUTTON2_Get();
if (temp_but2 && !old_but2) {
LED2_Set();
}
if (!temp_but2 && old_but2) {
LED2_Clear();
SERCOM1_USART_Virtual_Receive("iperf -s -u\n");
gfx_mono_print_scroll("iperf UDP server");
}
old_but2 = temp_but2;
static int old_but3 = 0;
int temp_but3 = BUTTON3_Get();
if (temp_but3 && !old_but3) {
LED3_Set();
}
if (!temp_but3 && old_but3) {
LED3_Clear();
SERCOM1_USART_Virtual_Receive("iperfk\n");
gfx_mono_print_scroll("iperf kill server");
}
old_but3 = temp_but3;
}
#include "config/default/peripheral/port/plib_port.h"
#include "config/default/peripheral/sercom/usart/plib_sercom1_usart.h"
#include "gfx_mono/gfx_definitions.h"

## Slide 15: Tips&Tricks: Set Programming Speed Up